## Slide 1
AUTOMATED BRAIN TISSUE SEGMENTATION
OF MAGNETIC RESONANCE IMAGES
IN MULTIPLE SCLEROSIS
SERGI VALVERDE
Dr. Arnau Oliver i Malagelada
Dr. Xavier Lladó i Bardera
INSTITUT DE RECERCA EN VISIÓ PER COMPUTADOR I ROBÒTICA – vicorob.udg.edu

## Slide 2
Human Brain
The human brain is composed of two main tissues: Gray matter (GM) and White matter (WM)
Gray matter
White matter
Neuron

## Slide 3
Multiple Sclerosis (MS) is the most common chronic neurological disease affecting the central nervous system (CNS)
MS is an auto-immune disease caused by the demyelination of the axons throught the CNS
Presence of lesions in the brain, mostly in the WM
Motor, sensorial, vision, coordination, deambulation, cognitive impairment
Multiple Sclerosis (MS)

## Slide 4
Multiple Sclerosis (MS)

## Slide 5
Magnetic Resonance Imaging (MRI)
Over the last 40 years, MRI has evolved as a clinical modality being an essential tool for the diagnosis and evaluation of CNS disorders such as MS
3D model of the brain as a stack of acquired 2D images
Images can be acquired at three orientations:
sagittal
coronal
axial
3D volume

## Slide 6
PD-w
T2-W
T1-W
In MRI, MS lesions are well-delimited regions with hypointense signal intensity with respect to Gray Matter (GM), while hyperintese signal intensity with respect to T2-w, PD-w and FLAIR
FLAIR
MRI and MS

## Slide 7
MRI and MS
Structural MRI provides evidence of the dissemination of WM lesions in space and time (McDonald criteria)
Correlation between MRI brain tissue atrophy and MS disability status, especially GM atrophy
12 month
baseline
lesions at time t
lesions at time t+1
new lesions
low atrophy
high atrophy
Greater ventricular
cavities
GM loss

## Slide 8
MRI and MS
Quantifying tissue loss permits to diagnose and monitorize the progression of the disease
Manual segmentation of brain tissue is challenging and time-consuming
Automated tissue segmentation
large number of MRI slices
inherent intra/inter-observer variability between experts
complexity of the images
lack of contrast between tissues
noise, intensity inhomogeneities
partial volume effects
the presence of WM lesions

## Slide 9
MRI and MS
The presence of WM lesions:
Tissue segmentation is performed in T1 as it provides the best contrast between tissues
Tissue classification into GM, WM and CSF
WM lesions affect tissue distributions
WM is classified
as GM
Healthy
MS patient

## Slide 10
Objectives
To develop a novel, fully automated brain tissue segmentation method capable of computing accurate tissue volume measurements in images of MS patients
To analyze and evaluate the state of the art of tissue segmentation methods
To study and evaluate the effect of WM lesions on tissue segmentation of MS patient images
To design and implement new automated algorithms to reduce the effect of WM lesions on tissue segmentation of MS patient images
To analyze and evaluate the effect of these algorithms in conjunction with automated WM lesion segmentation and filling on the tissue segmentation

## Slide 11
Outline
Analysis and evaluation of the state of the art in tissue segmentation
Evaluation of the effects of WM lesions on automated tissue segmentation
A new lesion filling algorithm to reduce the effects of WM lesions
Effect of automated lesion segmentation and filling on tissue segmentation
Automated brain tissue segmentation in the presence of WM lesions
Contributions and future work

## Slide 12
Outline
Analysis and evaluation of the state of the art in tissue segmentation
Evaluation of the effects of WM lesions on automated tissue segmentation
A new lesion filling algorithm to reduce the effects of WM lesions
Effect of automated lesion segmentation and filling on tissue segmentation
Automated brain tissue segmentation in the presence of WM lesions
Contributions and future work

## Slide 13
1. State of the art
Motivation:
To analyze and evaluate the state of the art of tissue segmentation methods
Understand their advantages and drawbacks first on images without MS lesions
We use public databases of
althy subjects that incorporate manual tissue annotations, which will allow us to perform a quantitative evaluation of the accuracy of the methods
Some of the methods incorporate automated skull-stripping and bias correction

## Slide 14
1. State of the art
Skull-stripping:
Usually, MRI Images have to be pre-processed first before tissue segmentation
Eyes, fat, spinal chord or the skull have to be extracted first
Bias field correction :
Differences in the magnetic field, movements of the patient inside the scanner
Pre-processing:

## Slide 15
1. State of the art
We evaluate 10 automated brain tissue segmentation methods:
Method reference | Algorithm characteristics |  |  |  | Version
Name | Algorithm | Image Type | IC | SS | Implementation
SPM5 (Ashburner 2005) | GMM + prior | all | yes | yes | SPM8 v.4667 (Feb 2012)
SPM8 (Ashburner 2005) | GMM + prior | all | yes | yes | SPM8 v.4667 (Feb 2012)
KNN (DeBoer 2009) | KNN + prior | T1,PD | no | no | MATLAB 7.12
GAMIXTURE (Tohka 2007) | GA-GMM | T1 | no | no | GAMIXTURE v1.1
ANN (Tian 2001) | SOM | T1 | no | no | MATLAB 7.12
FCM (Pham 2001a) | FCM | T1 | no | no | MATLAB 7.12
FAST (Zhang 2001) | HRMF+EM | all | yes | no | FSL v.5.0 (Sept 2012)
FANTASM (Pham 2001b) | RFCM | T1 | yes | yes | MIPAV v.R3c (Mar 2012)
PVC (Shattuck 2001) | MRF | T1 | yes | yes | Brainsuite 11.a (May 2011)
SVPASEG (Tohka2010) | GA-MRF | T1,T2 | no | no | v.2.1 (Oct 2010)
EM = Expectation Maximization, FCM = Fuzzy C-Means, GMM = Gaussian Mixture Model, GA = Genetic Algorithm,
HRMF = Hidden Random Markov Fields, MAP = Maximum-a-Posteriori, KNN = K-nearest Neighbor,
RFCM = Robust Fuzzy C-Means, SOM = Self Organized Map
IC = Intensity Correction, SS = Skull-stripping

## Slide 16
1. State of the art
Evaluated data:
IBSR20 image set is composed by 20 T1-w scans
  Image size: 256×23×256 (3.1 mm slice thickness)
  Labeled volumes with main tissue annotations for evaluation (GM, WM,CSF)
  Scans were corrected with N3
IBSR18 image set is composed by 18 T1-w scans
  Image size: 256×128×256 (1.5 mm slice thickness)
  Provided with Autoseg bias field correction
  Manually labeled volumes into 84 structures re-assigned into GM, WM, and CSF tissues)
2 datasets of normal subjects from the Internet Brain Segmentation Repository (IBSR)
In both datasets, sulcal CSF was not considered in the evaluation, as this was labeled as GM in the original annotations

## Slide 17
1. State of the art
Data analysis:
Dice coefficient between the GM, WM and CSF segmentation masks and the ground-truth annotations
IBSR20: DSC coefficients for each method (µ ± σ)
IBSR18: DSC coefficients for each method (µ ± σ)
Method | GM | WM | CSF
FAST | 0.82±0.06 | 0.78±0.12 | 0.76±0.12
SPM5 | 0.86±0.03 | 0.82±0.02 | 0.82±0.08
SPM8 | 0.86±0.06 | 0.81±0.07 | 0.83±0.08
GAMIXTURE | 0.83±0.06 | 0.74±0.16 | 0.75±0.10
ANN | 0.81±0.08 | 0.77±0.14 | 0.76±0.12
FCM | 0.81±0.08 | 0.77±0.14 | 0.76±0.12
KNN | 0.78±0.08 | 0.80±0.06 | 0.75±0.12
SVPASEG | 0.88±0.04 | 0.81±0.07 | 0.76±0.09
FANTASM | 0.81±0.08 | 0.77±0.14 | 0.77±0.12
PVC | 0.79±0.09 | 0.62±0.24 | 0.77±0.12
Method | GM | WM | CSF
FAST | 0.88±0.01 | 0.89±0.02 | 0.47±0.18
SPM5 | 0.89±0.02 | 0.87±0.02 | 0.79±0.08
SPM8 | 0.91±0.01 | 0.88±0.01 | 0.77±0.08
GAMIXTURE | 0.89±0.03 | 0.87±0.02 | 0.52±0.15
ANN | 0.87±0.03 | 0.88±0.03 | 0.52±0.15
FCM | 0.88±0.02 | 0.88±0.03 | 0.52±0.15
KNN | 0.87±0.03 | 0.86±0.03 | 0.46±0.16
SVPASEG | 0.90±0.01 | 0.87±0.02 | 0.57±0.13
FANTASM | 0.88±0.02 | 0.88±0.03 | 0.53±0.15
PVC | 0.83±0.08 | 0.84±0.07 | 0.52±0.15
Results:

## Slide 18
1. State of the art
Qualitative evaluation:
Tissue segmentation masks for IBSR_05 image (IBSR18): (a) Original image, (b) Ground-truth, and segmentation results from (C) FAST, (d) SPM5, (e) SPM8, (f) ANN, (g) FCM, (i) KNN, (j) SVPASEG, (k) FANTASM, and (l) PVC. CSF tissue is labeled in red, GM in green, and WM in blue

## Slide 19
1. State of the art
Conclusions:
A wide number of methods have been analyzed
SVPASEG, SPM5, SPM8 and FAST yielded the highest performance
This methods incorporated prior atlas information (SPM5/SPM8/SVPASEG) and spatial constraints (FAST) being more robust to noise and artifacts
However, the performance of most of the methods varied when segmenting GM structures, due to the lack of contrast and similar intensity profile with respect to WM
There was not a single method that achieved a significantly higher accuracy when compared to others in both GM and WM tissue

## Slide 20
Outline
Analysis and evaluation of the state of the art in tissue segmentation
Evaluation of the effects of WM lesions on automated tissue segmentation
A new lesion filling algorithm to reduce the effects of WM lesions
Effect of automated lesion segmentation and filling on tissue segmentation
Automated brain tissue segmentation in the presence of WM lesions
Contributions and future work

## Slide 21
2. Effect of WM lesions on segmentation
ANN, FCM, FANTASM, FAST, SPM5 and SPM8 methods were re-evaluated using MR images of MS patients in order to analyze the effect of WM lesions on tissue segmentation
As seen in the Introduction, WM lesions can affect tissue segmentation
WM is classified
as GM
MS patient

## Slide 22
3. Effect of WM lesions on segmentation
Evaluated data:
Lack of public available databases incorporating both manual tissue and lesion annotations
30 1.5T MRI images from patients with clinically confirmed MS at three different hospitals (H1= 10, H2 = 10 and H3 = 10) and scanners (Siemens, Phillips and GE)
T1-w images acquired in axial view (slice thickness of 3mm) along with manual lesion annotations
All T1-w images were skull-stripped using BET and bias-corrected using N3
WM lesions were manually delineated on the PD-w sequence

## Slide 23
2. Effect of WM lesions on segmentation
Masking-out:
A classical approach to deal with WM lesions has been masking-out them before segmentation and added as WM afterwards
Different approaches
have been proposed
In previous studies [ref, ref], filling WM lesions with signal intensities similar to normal-appearing WM has been shown to be effective reducing the effects of WM lesions on tissue segmentation
Local methods: signal intensities from neighboring voxels
Global methods: signal intensities from the whole image
Lesions are added
as WM

## Slide 24
3. Effect of WM lesions on segmentation
Data analysis:
ORIGINAL and MASKED sets were created from images with MS lesions:
T1-w scans
from
MS patients
skull
stripping
intensity
correction
scans with lesions
(ORIGINAL set)
scans without lesion
masks
(MASKED set)
(-)
(+)
segmented scans with lesions
lesion masks are added as WM in segmented scans without lesions

## Slide 25
3. Effect of WM lesions on segmentation
Method | H1 |  |  | H2 |  |  | H3 |  | 
 | GM | WM | CSF | GM | WM | CSF | GM | WM | CSF
ANN | 0.33±0.42 | -0.23±0.28 | 0.11±0.11 | 1.59±1.37 | -0.56±0.46 | 0.78±0.76 | 0.25±0.31 | -0.16±0.28 | -0.09±0.09
FCM | 0.28±0.37 | -0.22±0.29 | 0.09±0.11 | 2.28±2.26 | -0.90±0.83 | 0.94±0.90 | 0.28±0.23 | -0.25±0.20 | 0.08±0.09
FANTASM | 0.23±0.26 | -0.18±0.21 | 0.08±0.08 | 1.34±1.13 | -0.49±0.37 | 0.80±0.73 | 0.26±0.22 | -0.24±0.19 | 0.07±0.08
FAST | 0.29±0.36 | -0.29±0.36 | 0.12±0.13 | 1.92±1.59 | -1.28±1.03 | 0.47±0.39 | 0.34±0.28 | -0.37±0.31 | 0.12±0.17
SPM5 | 0.20±0.30 | -0.21±0.20 | -0.14±0.54 | 0.10±2.68 | -1.04±3.01 | 0.53±0.51 | 0.04±0.17 | -0.18±0.36 | 0.15±0.23
SPM8 | 0.08±0.09 | -0.08±0.08 | -0.04±0.18 | 0.55±0.34 | -0.93±0.55 | 0.54±0.42 | 0.09±0.15 | -0.23±0.25 | 0.17±0.23
Average % of change in total/normal-appearing tissue volume estimation between Original and Masked images. The results are divided by tissue and hospital. Reported values are µ ± σ. Positive values indicate a tissue overestimation on Original images compared to Masked
H1 |  |  | 
Method | GM | WM | CSF
ANN | 0.33±0.42 | -0.23±0.28 | 0.11±0.11
FCM | 0.28±0.37 | -0.22±0.29 | 0.09±0.11
FANTASM | 0.23±0.26 | -0.18±0.21 | 0.08±0.08
FAST | 0.29±0.36 | -0.29±0.36 | 0.12±0.13
SPM5 | 0.20±0.30 | -0.21±0.20 | -0.14±0.54
SPM8 | 0.08±0.09 | -0.08±0.08 | -0.04±0.18
H2 |  |  | 
Method | GM | WM | CSF
ANN | 1.59±1.37 | -0.56±0.46 | 0.78±0.76
FCM | 2.28±2.26 | -0.90±0.83 | 0.94±0.90
FANTASM | 1.34±1.13 | -0.49±0.37 | 0.80±0.73
FAST | 1.92±1.59 | -1.28±1.03 | 0.47±0.39
SPM5 | 0.10±2.68 | -1.04±3.01 | 0.53±0.51
SPM8 | 0.55±0.34 | -0.93±0.55 | 0.54±0.42
H3 |  |  | 
Method | GM | WM | CSF
ANN | 0.25±0.31 | -0.16±0.28 | -0.09±0.09
FCM | 0.28±0.23 | -0.25±0.20 | 0.08±0.09
FANTASM | 0.26±0.22 | -0.24±0.19 | 0.07±0.08
FAST | 0.34±0.28 | -0.37±0.31 | 0.12±0.17
SPM5 | 0.04±0.17 | -0.18±0.36 | 0.15±0.23
SPM8 | 0.09±0.15 | -0.23±0.25 | 0.17±0.23
Method | H1 |  |  | H2 |  |  | H3 |  | 
 | GM | WM | CSF | GM | WM | CSF | GM | WM | CSF
ANN | 0.15±0.26 | -0.10±0.18 | 0.07±0.08 | 0.70±0.61 | -0.31±0.24 | 0.67±0.69 | -0.01±0.28 | 0.04±0.24 | -0.12±0.08
FCM | 0.09±0.16 | -0.07±0.13 | 0.05±0.08 | 1.27±1.69 | -0.56±0.62 | 0.82±0.81 | 0.01±0.03 | -0.03±0.05 | 0.05±0.07
FANTASM | 0.06±0.05 | -0.05±0.05 | 0.03±0.05 | 0.48±0.48 | -0.25±0.18 | 0.68±0.63 | 0.00±0.04 | -0.02±0.05 | 0.04±0.07
FAST | 0.08±0.14 | -0.09±0.14 | 0.07±0.08 | 0.56±0.87 | -0.45±0.64 | 0.22±0.33 | 0.02±0.07 | -0.06±0.13 | 0.08±0.16
SPM5 | 0.06±0.25 | 0.02±0.13 | -0.19±0.54 | -0.29±2.61 | -0.47±2.91 | 0.21±0.32 | -0.20±0.24 | 0.23±0.34 | 0.06±0.15
SPM8 | -0.03±0.06 | 0.09±0.15 | -0.10±0.23 | 0.13±0.30 | -0.29±0.33 | 0.25±0.26 | -0.15±0.12 | 0.14±0.15 | 0.10±0.20
  % differences in tissue volume between Original and Masked images
% differences total tissue volume
% differences normal-appearing tissue volume
Results:
Notes: FIRST (TOTAL TISSUE)
Important EXPLICAR TABLE + - values overestimation/underestimation
SPM5/SPM8 where clearly the best methods
TAMBE NORMAL-APPEARING (estem interessats)
Still most of methods overestimated GM and underestimated WM
So lesions have an effect on the rest of tissue
SPM5/SPM8 +FANTASM where clearly the best methods

## Slide 26
3. Effect of WM lesions on segmentation
Qualitative evaluation:
A
B
C
D
E
F
G
H
Original image (A and B). ANN (C). FCM (D). FANTASM (E). FAST (F). SPM5 (G). SPM8 (H)

## Slide 27
3. Effect of WM lesions on segmentation
  Conclusions:
The main factor in the differences in tissue volume was lesion volume
All methods overestimated total GM volume by the addition of WM lesions in tissue segmentation
In general, SPM5, SPM8 and FANTASM were the methods where the incidence of WM lesions was the lowest on both total and normal-appearing tissue
When lesions were not considered in the evalution, methods still tended to overestimate GM, especially in images with a higher lesion load
This is important because although lesion voxels could be reassigned to WM after segmentation, part of the bias is still present in normal-appearing tissue

## Slide 28
Outline
Analysis and evaluation of the state of the art in tissue segmentation
Evaluation of the effects of WM lesions on automated tissue segmentation
A new lesion filling algorithm to reduce the effects of WM lesions
Effect of automated lesion segmentation and filling on tissue segmentation
Automated brain tissue segmentation in the presence of WM lesions
Contributions and future work

## Slide 29
3. Lesion filling
Different approaches
have been proposed
In previous studies [ref, ref], filling WM lesions with signal intensities similar to normal-appearing WM has been shown to be effective reducing the effects of WM lesions on tissue segmentation
Local methods: signal intensities from neighboring voxels
Global methods: signal intensities from the whole image
The results observed in the previous Section highlights the necessity of processing WM lesions before segmentation
Lesion filling provides a more optimal approach
Voxels from WM distribution
Lesion voxels are refilled with normal-appearing WM
Although effective, masking-out lesions before segmentation may not be optimal

## Slide 30
3. Lesion filling
Different approaches
have been proposed
In previous studies (Chard 2010, Battaglini 2012), it was shown that filling WM lesions with signal intensities similar to normal-appearing WM effective reduced the effects of WM lesions on tissue segmentation
Local methods: lesions are refilled using signal intensities from neighboring voxels (Sdika 2009, Battaglini 2012, Magon 2014)
Global methods: lesions are refilled using signal intensities from the whole image
(Chard 2010)

## Slide 31
3. Lesion filling
We propose a new lesion filling algorithm that combines both local and global information

## Slide 32
3. Lesion filling
Evaluation data:
OASIS dataset composed of 30 T1-w images
  1.5T T1-w images (256x256x128, slice thickness 1.25mm)
  We selected images from young and middle-aged subjects (age < 50)
  Skull-stripped using BET with Popescu 2012 optimization
  Images were already intensity corrected with N4
IXI dataset composed of 30 T1-w images
  3T T1-w images (256x256x150, slice thickness 1.20mm)
  Skull-stripped using BET with Popescu 2012 optimization
  Intensity correction using N4
Lesion generation:
  We used 37 MS patient images where lesions were registered randomly into WM to each of the 60 images
  Lesions were simulated by replacing lesion voxel intensities with signal intensities between GM and WM (normal distribution with mean GM , std GM / 4)

## Slide 33
3. Lesion filling
Data analysis:
For each database, we generated three initial sets:
NONE: the set of images with registered WM lesions
MASKED: the set of images where registered WM lesions were masked-out before segmentation
SLF: the set of images where registered WM lesions were lesion filled using our proposed approach
We also compared our proposed approach with three state-of-the art methods: MAGON (Magon 2014), FSL-L (Battaglini 2012) and LEAP (Chard 2010)

## Slide 34
3. Lesion filling
Volume analysis:
NONE
MASKED
MAGON
FSL
LEAP
SLF
original healthy
images
% of absolute difference in GM and WM
FAST/SPM8
segmentation
All methods were tested with both FAST and SPM8 tissue segmentation methods:
FAST/SPM8
segmentation

## Slide 35
3. Lesion filling
Results:
OASIS dataset (1.5T)
FAST
SPM8
Statistical significance by ranking methods with pair-wise permutation tests:
 | NGMV |  |  | NWMV | 
 | Method | µ ± σ |  | Method | µ ± σ
Rank 1 | SLF | 0.83±0.41 |  | SLF | 0.83±0.41
Rank 2 | FSL-L | 0.33±0.82 |  | FSL-L | 0.33±0.82
 | LEAP | 0.33±0.82 |  | LEAP | 0.33±0.82
Rank 3 | MAGON | -0.17±0.98 |  | MAGON | -0.17±0.98
 | MASKED | -0.23±0.41 |  | MASKED | -0.23±0.41
 | NONE | -0.50±0.84 |  | NONE | -0.50±0.84
FAST segmentation
 | NGMV |  |  | NWMV | 
 | Method | µ ± σ |  | Method | µ ± σ
Rank 1 | SLF | 0.67±0.52 |  | SLF | 0.83±0.41
 | LEAP | 0.67±0.52 |  |  | 
Rank 2 | MAGON | 0.00±0.89 |  | LEAP | 0.33±0.82
 | FSL-L | 0.00±0.89 |  | MAGON | 0.17±0.75
Rank 3 | NONE | -0.67±0.52 |  | FSL-L | 0.00±0.89
 | MASKED | -0.67±0.52 |  | MASKED | -0.50±0.84
 |  |  |  | NONE | -0.83±0.41
SPM8 segmentation

## Slide 36
3. Lesion filling
Results:
IXI dataset (3T)
FAST
SPM8
Pair-wise permutation tests:
 | NGMV |  |  | NWMV | 
 | Method | µ ± σ |  | Method | µ ± σ
Rank 1 | SLF | 0.67±0.52 |  | SLF | 0.67±0.52
 | LEAP | 0.66±0.51 |  | LEAP | 0.50±0.55
 |  |  |  | FSL-L | 0.33±0.82
Rank 2 | MAGON | 0.00±0.8 |  | MAGON | -0.17±0.98
 | FSL-L | 0.00±0.3 |  |  | 
Rank 3 | MASKED | -0.50±0.84 |  | MASKED | -0.50±0.84
 | NONE | -0.83±0.41 |  | NONE | -0.83±0.41
FAST segmentation
SPM8 segmentation
 | NGMV |  |  | NWMV | 
 | Method | µ ± σ |  | Method | µ ± σ
Rank 1 | LEAP | 0.67±0.52 |  | LEAP | 0.67±0.52
 | SLF | 0.67±0.52 |  | SLF | 0.67±0.52
 | MAGON | 0.17±0.98 |  | MAGON | 0.17±0.98
Rank 2 | FSL-L | -0.33±0.81 |  | FSL-L | -0.17±0.98
 | MASKED | -0.33±0.81 |  |  | 
Rank 3 | NONE | -083±0.41 |  | MASKED | -0.50±0.84
 |  |  |  | NONE | -0.83±0.41

## Slide 37
3. Lesion filling
Qualitative evaluation:
A
B
C
D
E
F
Original image (A-B). FSL-L (C). MAGON (D). LEAP (E). SLF (F)

## Slide 38
3. Lesion filling
Conclusions:
Differences in tissue volume with either FAST or SPM8 were very low (< 0.1%)
SLF yielded the lowest deviation in GM and WM volumes with 1.5T and 3T data when FAST tissue segmentation was used
SLF was very competitive when SPM8 was used, with lowest differences or similar to those of the best method
SLF was equally efficient independently of the tissue segmentation chosen
The proposed algorithm performed significantly better than local methods on images with high lesion load, and equal or better than global, specially on 1.5T data

## Slide 39
Outline
Analysis and evaluation of the state of the art in tissue segmentation
Evaluation of the effects of WM lesions on automated tissue segmentation
A new lesion filling algorithm to reduce the effects of WM lesions
Effect of automated lesion segmentation and filling on tissue segmentation
Automated brain tissue segmentation in the presence of WM lesions
Contributions and future work

## Slide 40
4. Lesion segmentation and filling
As seen in the previous Section, automated lesion filling is effective reducing the effects of WM lesions on tissue segmentation
However, manual lesion annotations have to be usually delineated first, which can be both tedious and time-consuming
Labeled data may be not available which highlights the interest in evaluating the effect of automated lesion segmentation and filling on tissue segmentation
FLAIR
T1-w
MANUAL
ANNOTATIONS
Lesion filling
Tissue segmentation
output
segmentation
Automated lesion segmentation

## Slide 41
4. Lesion segmentation and filling
Lesion segmentation:
Usually performed in T2-w, PD or FLAIR
Lesions appear hyperintense with respect to GM and WM
Intensity signal
GM
Lesions
Numerous approaches:
supervised: statistical classifiers, patch-based models, etc…
unsupervised: probabilistic models, thresholding, etc…

## Slide 42
4. Lesion segmentation and filling
In this Section, we evaluate two state-of-the-art pipelines incorporating automated unsupervised lesion segmentation and filling as prior step to SPM8 tissue segmentation
SLS pipeline (Cabezas 2014, Roura 2015):
Lesion segmentation: Unsupervised segmentation based on thresholding of GM hyperintensities with posterior regionwise reﬁnement (T1-w and FLAIR)
Lesion filling: SLF method as proposed in the previous Section (Valverde 2014)
LST pipeline (Schmidt 2012):
Lesion segmentation: Unsupervised lesion segmentation based on an iterative refinement of the likelihood of candidates to belong to either GM or lesions (T1-w and FLAIR)
Lesion filling: Global approach inspired by the LEAP (Chard 2010)

## Slide 43
4. Lesion segmentation and filling
Data analysis:
For both the LST and SLS, the following pipelines were defined:
T1-w
Automated
Lesion filling (SLF)
Tissue segmentation
(SPM8)
MANUAL EXPERT
ANNOTATIONS
T1-w
Tissue segmentation
(SPM8)
Pipeline | Lesion segmentation | Lesion filling
1.Original | - | -
2.Expert Masked | Manual | Expert annotations are masked
3.SLS Masked | SLS | SLS lesion masks are masked
4.SLS Filled | SLS | SLS lesion masks are filled by SLF
5.Expert Filled (GT) | Manual | Expert annotations are filled by SLF
Original
Expert Masked
SLS Masked
SLS Filled
Expert Filled (GT)

## Slide 44
4. Lesion segmentation and filling
Evaluation data:
70 Clinically Isolated Syndrome (CIS) patients clearly suggestive of MS from the Vall d’Hebron Hospital, Barcelona
3T T1-MPRAGE , PD-w and FLAIR were provided
Images were skull-stripped using BET and intensity normalized using N3
WM lesions were manually delineated by an expert technician in either PD-w (46 scans) and FLAIR (24 scans)

## Slide 45
4. Lesion segmentation and filling
Results:
The Δ symbol depicts the mean % difference in total GM/WM tissue for each pipeline. Horizontal lines show significant differences in Repeated ANOVA tests between evaluated pipelines with * = p<0.05, ** = p<0.01, *** = p < 0.001.
GM tissue
WM tissue

## Slide 46
5. Lesion segmentation and filling
Results:
input T1-w (A), input FLAIR (B), T1-w with expert annotations highlighted in blue (C), and T1-w output segmentation for the Expert filled image with CSF, GM and WM voxels depicted in black, gray, and white, respectively. Differences in any tissue classes for the Original SLS (E) , Masked (F), SLS Masked (G), and SLS Filled (H) , Original LST (E), LST Masked (F), LST Masked (G), and LST Filled (H)

## Slide 47
4. Lesion segmentation and filling
Conclusions:
Automated pipelines significantly reduced the impact of WM lesions on tissue segmentation
Masked effect between total and normal-appearing tissue volume
False negative lesion voxels were the main cause of errors
Lesion filling reduced the differences in tissue volume on the SLS and LST pipelines when compared to masked
The differences in tissue volume in images processed with fully automated pipelines was similar to pipelines incorporating manual intervention

## Slide 48
Outline
Analysis and evaluation of the state of the art in tissue segmentation
Evaluation of the effects of WM lesions on automated tissue segmentation
A new lesion filling algorithm to reduce the effects of WM lesions
Effect of automated lesion segmentation and filling on tissue segmentation
Automated brain tissue segmentation in the presence of WM lesions
Contributions and future work

## Slide 49
5. MSSEG: tissue segmentation in MS
From previous Sections, several insights can be sumarized in order to deal with automated brain tissue segmentation in the presence of MS lesions:
T1-w
Lesion
filling
Accurate
GM,WM,CSF
FLAIR
Automated lesion
estimation

## Slide 50
5. MSSEG: tissue segmentation in MS
Proposed method:
T1-w
FLAIR
5 class
segmentation
Estimate and refill WM outliers
Hyperintense
map
Tissue
seg
5 class
segmentation
Register priors
Notes: MOTIVATION MULTICHANNEL

## Slide 51
5. MSSEG: tissue segmentation in MS
Proposed method:
T1-w
Register priors

## Slide 52
5. MSSEG: tissue segmentation in MS
Register atlas priors to T1-w space
The MNI-ICBM 152 2009a Nonlinear T1-w template was affine + non-rigidly with a fast free-form deformation method (Ourselin 2002, Modat 2010)
Transformation parameters obtained were then used to resample the available MNI CSF, GM and WM tissue priors to the T1-w space
The resampled probabilistic tissue maps were extended to build intermediate partial volumes CSFGM and GMWM
Also, a morphological brain structure atlas of cortex, ventricles, basal ganglia and brainstem was parcellated on the original MNI atlas using the hierarchical algorithm proposed by Pohl et al. (2007)

## Slide 53
5. MSSEG: tissue segmentation in MS
Proposed method:
T1-w
5 class
segmentation
Register priors

## Slide 54
5. MSSEG: tissue segmentation in MS
Tissue estimation:
Brain tissue was estimated following a robust fuzzy-clustering approach similar to the FANTASM approach proposed in Pham (2001)
3 class
5 class
but spatial penalizing weights incorporating the probabilistic tissue priors were added
Signal intensity
WM
GM
CSF
Signal intensity
WM
GM
CSF
GMWM
CSFGM

## Slide 55
5. MSSEG: tissue segmentation in MS
Proposed method:
T1-w
FLAIR
5 class
segmentation
Estimate and refill WM outliers
Hyperintense
map
Register priors

## Slide 56
5. MSSEG: tissue segmentation in MS
Estimate and refill WM outliers
T1 5 class segmentation
FLAIR image
process each class
GMWM, GM, CSFGM
Compute all 2D regions
process each region
cortex?
Compute probability
of the region to WM
Compute probability
of neighbors to WM
Refill?
Refill region as WM
Add the current
region to WM ROI
End of outlier estimation
Estimate hyper-intense regions
Compute all 3D regions
Overlap?
Extract best hyper-intense region
Compute probability
of neighbors to GMWM / WM
Refill?
CSFGM
GM
GMWM
Hyper-intense
regions
no
yes
yes
yes
yes

## Slide 57
5. MSSEG: tissue segmentation in MS
Proposed method:
T1-w
FLAIR
5 class
segmentation
Estimate and refill WM outliers
Hyperintense
map
5 class
segmentation
Register priors

## Slide 58
5. MSSEG: tissue segmentation in MS
Re-estimate tissue:
After detect and refill all WM outliers, images are segmented again in 5 clases in order to preserve a better contrast between structures
Input T1
WM outlier detection and filling
Refilled T1
Tissue segmentation
with lesions
Tissue segmentation
corrected

## Slide 59
5. MSSEG: tissue segmentation in MS
Proposed method:
T1-w
FLAIR
5 class
segmentation
Estimate and refill WM outliers
Hyperintense
map
Tissue
seg
5 class
segmentation
Register priors

## Slide 60
5. MSSEG: tissue segmentation in MS
Output segmentation:
Finally, CSFGM and GMWM clases are re-assigned into CSF, GM and WM
2D regions with at least half of their area overlapping one of the structures of the atlas are reassigned to this particular tissue
The rest of voxels are reassigned to the most similar local class

## Slide 61
5. MSSEG: tissue segmentation in MS
Data analysis:
We compare the performance of our approach with two databases of images containing lesions:
MICCAI MRBrainS13 challenge database:
20 scans with varying degrees of brain atrophy and WM lesions
3T 3D T1-w, T1-IR and FLAIR
Images were already intensity-corrected
Tissue segmentation masks were manually delineated by 3 experts
  5 scans were provided with annotations for training
  15 were blind and used to evaluate each of the participant strategies

## Slide 62
5. MSSEG: tissue segmentation in MS
Evaluation (MRBrainS13 database):
Provided ground truth of labelled tissue permits to compute the performance of the method with respect to expert manual annotations
Dice coefficient:
Absolute difference in tissue volume:

## Slide 63
5. MSSEG: tissue segmentation in MS
Results: (MRBrainS13 database)
Method | CSF | GM | WM | CSF | GM | WM | Rank
Best method |  |  |  |  |  |  | 1
FAST only T1 |  |  |  |  |  |  | 21
SPM12 only T1 |  |  |  |  |  |  | 20
SPM12 T1+FLAIR |  |  |  |  |  |  | 17
SPM12 T1-iR |  |  |  |  |  |  | 18
VBM12 |  |  |  |  |  |  | 8
MSSEG only T1 |  |  |  |  |  |  | 10
MSSEG T1+FLAIR |  |  |  |  |  |  | 7
Method | CSF | GM | WM | CSF | GM | WM | Rank
Best method |  |  |  |  |  |  | 1
FAST only T1 |  |  |  |  |  |  | 21
SPM12 only T1 |  |  |  |  |  |  | 20
SPM12 T1+FLAIR |  |  |  |  |  |  | 17
SPM12 T1-iR |  |  |  |  |  |  | 18
VBM12 |  |  |  |  |  |  | 8
MSSEG only T1 |  |  |  |  |  |  | 10
MSSEG T1+FLAIR |  |  |  |  |  |  | 7
DSC coefficient
% dif abs volume

## Slide 64
5. MSSEG: tissue segmentation in MS
Data analysis (MS database):
24 CIS patients from the same hospital center
3T T1-MPRAGE and FLAIR were obtained for each of the patients
WM lesions were manually delineated by an expert technician in FLAIR. No manual label tissue annotations available
FLAIR and manual lesion masks were linearly corregistered into T1-w space
Images were skull-stripped using BET and intensity normalized using N3

## Slide 65
5. MSSEG: tissue segmentation in MS
Evaluation (MS database):
Absolute difference in tissue volume:
Percentage of misclassification:
Same type evaluation
used in previous
Section 4
Pipeline | Modality | Lesion seg. | Lesion filling | Tissue seg.
1. FAST only T1 | T1 | none | none | FAST
2. FAST + SLS | T1, FLAIR | SLS (FLAIR) | SLF | FAST
3. FAST GT | T1 | expert manual | SLF | FAST
4. SPM12 only T1 | T1 | none | none | SPM12
5. SPM12 + SLS | T1, FLAIR | SLS (FLAIR) | SLF | SPM12
6. SPM12 GT | T1 | expert manual | SLF | SPM12
7. MSSEG only T1 | T1 | internal | internal | MSSEG
8. MSSEG T1 + FLAIR | T1, FLAIR | internal | internal | MSSEG
9. MSSEG GT | T1 | expert manual | SLF | MSSEG

## Slide 66
5. MSSEG: tissue segmentation in MS
Results (MS database):
% dif abs volume
Tissue segmentation masks for the MS subject 4 of the 3T dataset. A) Original T1-w image. B) Original T1-w with MS lesions depicted in red. C) FAST only T1 segmentation. D) FAST + SLS segmentation. E) SPM12 only T1 segmentation. F) SPM12 + SLS segmentation. G) MSSEG only T1 segmentation. H) MSSEG T1+FLAIR segmentation
Method | Dif CSF (%) | Dif GM (%) | Dif WM (%) | CSF (%) | GM (%) | WM (%)
FAST only T1 | 0.07 ± 0.13 | 0.33 ± 0.45 | 0.42 ± 0.56 | 0.08 ± 0.11 | 0.09 ± 0.12 | 0.53 ± 0.69
FAST + SLS | 0.04 ± 0.07 | 0.08 ± 0.12 | 0.11 ± 0.16 | 0.06 ± 0.06 | 0.14 ± 0.16 | 0.25 ± 0.30
SPM12 only T1 | 0.31 ± 0.46 | 0.27 ± 0.45 | 0.56 ± 0.69 | 0.16 ± 0.32 | 0.25 ± 0.33 | 0.73 ± 0.86
SPM12 + SLS | 0.22 ± 0.22 | 0.13 ± 0.23 | 0.20 ± 0.32 | 0.22 ± 0.31 | 0.24 ± 0.29 | 0.41 ± 0.43
MSSEG only T1 | 0.13 ± 0.20 | 0.21 ± 0.26 | 0.42 ± 0.54 | 0.02 ± 0.03 | 0.03 ± 0.05 | 0.46 ± 0.58
MSSEG T1+FLAIR | 0.04 ± 0.05 | 0.06 ± 0.05 | 0.13 ± 0.11 | 0.04 ± 0.04 | 0.14 ± 0.13 | 0.27 ± 0.29
% of misclassification

## Slide 67
5. MSSEG: tissue segmentation in MS
Conclusions:
MSSEG yields competitive and consistent results in both general and MS specific databases
The addition of the FLAIR modality increases the performance of the method
With MRBrainS13 data, our method is the best non-supervised intensity model method (7th ranked out of 31 participants / 10th using only T1-w)
The combination of intensity, anatomical and morphological priors, and the use of a specific outlier algorithm with integrated lesion filling improves segmentation
With MS data, the performance was similar or better than the best evaluated pipeline incorporating automated lesion segmentation and filling
The low differences in tissue volume validates the capability of MSSEG reducing the effects of WM lesions on tissue segmentation

## Slide 68
Outline
Analysis and evaluation of the state of the art in tissue segmentation
Evaluation of the effects of WM lesions on automated tissue segmentation
A new lesion filling algorithm to reduce the effects of WM lesions
Effect of automated lesion segmentation and filling on tissue segmentation
Automated brain tissue segmentation in the presence of WM lesions
Contributions and future work

## Slide 69
Contributions and future work
This doctoral thesis is a compendium of the following articles:
S. Valverde, A. Oliver, M. Cabezas, E. Roura, X. Lladó. "Comparison of ten brain tissue segmentation methods using revisited IBSR annotations". Journal of Magnetic Resonance Imaging, 41(1), pp. 93-101. 2015.
[JCR RNMMI IF: 3.210 Q1(23/125)]
Section 2: the evaluation of the effects of WM lesions in different tissue segmentation methods
S. Valverde, A. Oliver, Y. Díez, M. Cabezas, J.C. Vilanova, Ll. Ramió-Torrentà,
À. Rovira, and X. Lladó. "Evaluating the effects of white matter multiple
sclerosis lesions on the volume estimation of six brain tissue segmentation methods". American Journal of Neuroradiology, 36(6), pp. 1109-115, 2015.
[JCR RNMMI IF 3.589, Q1(19/125)]
Section 1: the state of the art in automated tissue segmentation

## Slide 70
Contributions and future work
This doctoral thesis is a compendium of the following articles:
Section 4: analysis to the effects of automated brain lesion segmentation and filling on the tissue volume measurements of MS patient images
Section 3: a new framework to refill WM lesions before segmentation
S. Valverde, A. Oliver, X. Lladó. "A white matter lesion-filling approach to improve brain tissue volume measurements". NeuroImage: Clinical, (6), pp 86-92, 2014. [JCR N IF 2.526, Q2(6/14)]
S. Valverde, A. Oliver, E. Roura, D. Pareto, J.C. Vilanova, Ll. Ramió-Torrentà, J. Sastre-Garriga, X, Montalban, À. Rovira, and X. Lladó. "Quantifying brain
tissue volume in multiple sclerosis with automated lesion segmentation and filling". NeuroImage: Clinical, (9), pp 640-647, 2015
[JCR N IF 2.526, Q2(6/14)]

## Slide 71
Contributions and future work
This doctoral thesis is a compendium of the following articles:
Section 5: automated brain tissue segmentation in the presence of MS lesions
S. Valverde, A. Oliver, E. Roura, S. González, D. Pareto, JC Vilanova,
L. Ramió-Torrentà, À. Rovira and X. Lladó. “Automated brain tissue segmentation of MR images in the presence of white matter lesions”. Medical Image analysis. (2nd revision) 2016. Elsevier.
[JCR CSAI IF 3.654, Q1 (10/121)]

## Slide 72
Contributions and future work
Related to our work, several contributions to other journal articles have been done during the PhD program:
S. González, A.Oliver, S.Valverde, L. Wang, R. Zwiggelaar and X.Lladó. “A review of brain structures segmentation in magnetic resonance imaging”. Artificial Intelligence in medicine (2nd revision). 2016. [IF 2.019, Q2(40/123) CSAI]
E. Roura, N. Sarbu, A. Oliver, S. Valverde, S. González, R. Cervera, N. Bargalló and X. Lladó. Automated detection of Lupus white matter lesions in MRI images. Frontiers in Human Neuroscience (2nd revision). 2016. [JCR PS IF 3.626, Q1(13/76)].
E. Roura, A. Oliver, M. Cabezas, S. Valverde, D. Pareto, J.C. Vilanova, Ll. Ramió-Torrentà, À. Rovira, and X. Lladó. "A toolbox for multiple sclerosis lesion segmentation". Neuroradiology, pp. 1031-1043. 2015. [JCR RNMMI IF 2.485, Q2(41/125)]
M. Cabezas, A. Oliver, S. Valverde, B. Beltran, J. Freixenet, J.C. Vilanova, Ll. Ramió-Torrentà, À. Rovira, and X. Lladó. "BOOST: a supervised approach for multiple sclerosis lesion segmentation". Journal of Neuroscience Methods, 237, pp 108-117, 2014. [JCR N IF 2.025, Q3(174/252)]
Y. Diez, A. Oliver, M. Cabezas, S. Valverde, R. Martí, J.C. Vilanova, Ll. Ramió-Torrentà, A. Rovira, and X. Lladó. "Intensity based methods for brain MRI longitudinal registration. A study on multiple sclerosis patients". Neuroinformatics, 12(3), pp 365-379, 2014. [JCR CSTM IF 2.825, Q1(13/102)]

## Slide 73
Contributions and future work
Finally, several contributions to scientific conferences have been also possible:
[MS 2015] S. Valverde, A. Oliver, E. Roura, D. Pareto, J.C. Vilanova, Ll. Ramió-Torrentà, J. Sastre-Garriga, X, Montalban, À. Rovira, and X. Lladó. "Evaluation of two automated lesion segmentation and filling pipelines for brain tissue segmentation of multiple sclerosis patients". Multiple Sclerosis, Barcelona. October 2015. [JCR CN IF:4.822 Q1(22/192)]
[MS 2015] E. Roura, A. Oliver, M. Cabezas, S. Valverde, D. Pareto, J.C. Vilanova, Ll. Ramió-Torrentà, À. Rovira, and X. Lladó. "A toolbox for segmenting multiple sclerosis lesions using T1w and FLAIR images". Multiple Sclerosis, Barcelona. October 2015. [JCR CN IF:4.822 Q1(22/192)]
[NE 2014] E Quintana, B Beltrán, S Valverde, R Robles-Cedeño, H. Perkal, X. Lladó, JM Fernández-Real, Ll. Ramió-Torrentà "Relacion entre la expresion de mirnas en LCR y variables de RM". Neurología, pp 66-67, vol 29, 2014.
[JCR CN IF:1.322 Q3(142/191)]
[MS 2014] S. Valverde, A. Oliver, D. Pareto, J.C. Vilanova, À. Rovira, Ll. Ramió-Torrentà, and X. Lladó. "SLF: a MS white matter lesion filling toolbox for the SPM software". Multiple Sclerosis, pp296, 20(S1), Boston, Massachusetts. September 2014. [JCR CN IF:4.822 Q1(22/192)]
[MS 2014] E Quintana, B Beltrán, S Valverde, R Robles-Cedeño, H. Perkal, X. Lladó, JM Fernández-Real, Ll. Ramió-Torrentà "Expression of miRNAs in multiple sclerosis cerebrospinal fluid and their relation to MR activity".
Multiple Sclerosis, pp191, 20(S1), Boston, Massachusetts. September 2014. [JCR CN IF:4.822 Q1(22/192)]
[MS 2013] S.Valverde, A. Oliver, M. Cabezas, Y. Díez, J. Freixenet, X. Lladó, J.C. Vilanova, A. Rovira and Ll. Ramió-Torrentà. "A quantitative study of the effects of White Matter MS Lesions on tissue segmentation methods". Multiple Sclerosis. 19(S1), pp 407-408. Copenhagen, Denmark. 2-5 October 2013. [JCR CN IF:4.472 Q1(25/191)]

## Slide 74
Contributions and future work
Future work:
Although the proposed tissue segmentation method has been designed for cross-sectional data, there is an increasing clinical interest in the measuring of longitudinal changes in tissue volume
1. The proposed method could be extended to longitudinal changes by re-adapting the pipeline with prior registering of time point images before the tissue segmentation
2. Implementation of the developed tools in the collaborating research centers
3. Supervised strategies for automated tissue and lesion segmentation

## Slide 75
Acknowledgments
Dr. Ll. Ramió, A. Quiles,
G. Laguillo, B. Beltrán
Dr. J.C. Vilanova
Dr. J. Barceló
A. Rovira, Dra. D. Pareto,
J. Sastre-Garriga, X. Montalban
Collaborators:
TIN2014-55710-R

## Slide 76
AUTOMATED BRAIN TISSUE SEGMENTATION
OF MAGNETIC RESONANCE IMAGES
IN MULTIPLE SCLEROSIS
SERGI VALVERDE
Dr. Arnau Oliver i Malagelada
Dr. Xavier Lladó i Bardera
INSTITUT DE RECERCA EN VISIÓ PER COMPUTADOR I ROBÒTICA – vicorob.udg.edu

## Slide 77
Annexes

## Slide 78
Statisical ranking of the methods based on their DSC accuracy using pair-wise permutation tests (Klein 2009, Diez 2014)
permutation test algorithm:
Select a pair of methods (two vectors of P total DSC values)
Subtract the two vectors and compute the mean difference D
Select a subset of the elements from one of the vectors
Swap this subset across the two vectors
Subtract the resulting vectors; compute the mean difference Dp
Repeat steps #4–6 N times
Count the number of times n where abs(Dp)≥abs(D)
Compute the exact p-value: p=n / N
Repeat steps #1–9; compute the fraction of times where p≤0.05.
The test returns the µ and σ of the fraction of times when each method provides a higher DSC value than the rest of the methods with significant (p-value < 0.05)
Methods with higher means have passed a higher number of pairwise comparisons with other methods using randomly chosen subsets of values
Ranks are decided in terms of the distance of the µ of each method to the best mean observed (µ0, σ0)
  Rank 1 methods are those in (µ0 – σ0 , µ0 ],
  Rank 2 methods fall in (µ0 - 2σ0 , µ0 -σ0] and
  Rank 3 methods are those in the interval (µ0 -3σ , - µ0 -2σ ]
In all our experiments we have repeated the permutation tests within N=1000
Permutation tests (explanation)

## Slide 79
1. State of the art (supplementary data)
Permutation tests:
IBSR20 (not considering sulcal CSF) |  |  |  |  | 
 | GM |  |  | WM | 
 | Method | µ ± σ |  | Method | µ ± σ
Rank 1 | SVPASEG | 0.80±0.42 |  | SVPASEG | 0.64±0.48
 | SPM5 | 0.70±0.48 |  | SPM8 | 0.60±0.52
 | SPM8 | 0.60±0.70 |  | SPM5 | 0.50±0.53
 |  |  |  | KNN | 0.46±0.58
 |  |  |  | FAST | 0.30±0.82
Rank 2 | GAMIXTURE | 0.30±0.95 |  | ANN | -0.30±0.82
 | FAST | 0.10±0.99 |  | FANTASM | -0.30±0.82
 |  |  |  | FCM | -0.30±0.82
Rank 3 | FANTASM | -0.19±0.92 |  | GAMIXTURE | -0.70±0.67
 | ANN | -0.50±0.71 |  | PVC | -0.90±0.32
 | FCM | -0.50±0.71 |  |  | 
 | PVC | -0.51±0.52 |  |  | 
 | KNN | -0.80±0.42 |  |  | 
 | IBSR18 (not considering sulcal CSF) |  |  |  |  |  | 
 |  |  | GM |  |  | WM | 
 |  |  | Method | µ ± σ |  | Method | µ ± σ
 | Rank 1 |  | SPM8 | 0.70±0.48 |  | FAST | 0.90±0.32
 |  |  | SVPASEG | 0.60±0.52 |  |  | 
 |  |  | FAST | 0.40±0.70 |  |  | 
 |  |  | GAMIXTURE | 0.32±0.47 |  |  | 
 | Rank 2 |  | FANTASM | 0.10±0.74 |  | SPM8 | 0.38±0.68
 |  |  | FCM | -0.22±0.79 |  |  | 
 | Rank 3 |  | KNN | -0.29±0.49 |  | FCM | 0.25±0.63
 |  |  | SPM5 | -0.32±0.64 |  | FANTASM | 0.24±0.63
 |  |  | ANN | -0.50±0.71 |  | ANN | 0.24±0.63
 |  |  | PVC | -0.79±0.41 |  | SPM5 | -0.20±0.42
 |  |  |  |  |  | KNN | -0.33±0.40
 |  |  |  |  |  | GAMIXTURE | -0.38±0.68
 |  |  |  |  |  | SVPASEG | -0.50±0.53
 |  |  |  |  |  | PVC | -0.60±0.52
IBSR20 dataset:
IBSR18 dataset:
Permutation tests for obtained Dice overlap coefficients on the IBSR20/18 dataset with original ground-truth and not considering sulcal CSF voxels. Reported values are mean and standard deviation (μ, σ) of the fraction of times when each method produced significant p-values. Positive values indicate that on average , the method over-performed the other methods in pair-wise significant tests

## Slide 80
2. Effect of WM lesions (supplementary data)
Results:
  % of WM lesion voxels classified as GM or WM between Original and Masked images:
  Classification output returned by each segmentation method on the same image. (a) T1-w scan. (b) Zoomed part of the scan with lesions outlined in red. Brain tissue segmentation outputs also with lesions outlined for (c) ANN, (d) FCM, (e) FANTASM, (f) FAST, (g) SPM5, and (h) SPM8. On images (c-h), segmented GM tissue is represented in gray, WM in white and CSF in black.
  Percentage µ ± σ of voxels in WML regions having been classified as GM (Fig top) and WM (Fig bottom) for each segmentation method and hospital H1 (⋄), H2 (□) and H3 (o)
H1
H2
H3

## Slide 81
4. Lesion segmentation and filling (supp.)
Additional data:

## Slide 82
4. Lesion segmentation and filling (supp.)
Masking effect between normal-appearing and lesion differences:
lesions are either classified
as GM or WM
Lesions  GM cause under-segmentation of WM
Lesions  WM reduce the boundary between GM/WM causing other voxels with GM intensity to be classified as WM!!!!

## Slide 83
4. Lesion segmentation and filling (supp.)
% differences in normal-appearing tissue volume (grouped by lesion size):

## Slide 84
5. MSSEG (Motivation)
Tissue segmentation:
A modified Fuzzy-C-Means approach was choosen for the signal intensity model:
Advantages | Drawbacks
Straightforward implementation | FCM assumes clusters of the same size (minimized by atlas-based initialization)
fairly robust behavior including spatial context information | Less popular than generative
Spatial constraints are similar to MRF spatial priors | Less elegant when compared with generative models
Modeling of uncertainity via membership functions | 
Very fast when compared with other methods | 
Easy to vectorize and implement in a GPU | 
this method provides a straightforward implementation
- fairly robust behavior including spatial context information
- applicability to multichannel data
- the ability to model uncertainty within the data
- FAST when compared to other models --> capability of vectorize in MATLAB --> GPU use
- Similarity with SPM
- These are usually similar to the expectation-maximization algorithm for mixtures of Gaussian distributions via an iterative refinement approach employed by both algorithms

## Slide 85
5. MSSEG (Formulation)
Tissue segmentation:
Objective function:
An iterative algorithm is used to minimize (1) by evaluating the centroids and functions that satisfy a zero gradient condition:
q = 2, w = 1, and gamma = 1/10 in all experiments

## Slide 86
5. MSSEG (Formulation)
Tissue segmentation:
The derived membership function used in algorithm (1):
Five class segmentation was computed by:

## Slide 87
5. MSSEG (Outlier estimation and filling)
Define binary masks GMWM, GM and CSFGM
Compute all 2D regions with (first level neighborhood)
Compute hyper-intense map on the FLAIR image
Compute all 3D regions with (first level neighborhood)

## Slide 88
5. MSSEG (Partial classes)
CSFGM and GMWM classes are re-assigned to either CSF, GM and WM by:
2D regions of connected components from each binary mask
Overlap with respect to the morphological atlas
Voxels not re-assigned in the last step are classified with respect to their most similar local class
(in all experiments, j = 6 in 2D)

## Slide 89
5. MSSEG (supplementary data)
Permutation tests on MS data:

## Slide 90
5. MSSEG (supplementary data)
% error in lesion voxels